## Slide 1: Hocus Focus
George Hilios
NEAIC, Suffern NY
April 14, 2023
The Science of Star Measurement for
Auto-Focusing and Tilt Correction

## Slide 2: Familiar Situation?

## Slide 3: Hocus Focus
Optimize performance for amateur astronomy
  Pinpoint focus
  Fast: Minimize image acquisition impact
  Sophisticated: Fine tune back-focus and tilt
Promote scientific discourse and discovery
  No ivory towers: test theories with data
Transparent algorithms
  No magic parameters!
  Fully open source (MPLv2)

## Slide 4: About Myself

## Slide 5: NINA Contributions
Dome support, including scope synchronization
Center after Drift
MetaGuide integration
SBIG CCD native support
Plugins
  Orbitals: tracking and imaging comets, asteroids, planets
  10u Tools: building models for 10 micron mounts
  Hocus Focus: Auto focus, PSF measurement, aberration inspection

## Slide 6: Agenda
Scientific Workbench
Star Measurement
Finding Optimal Focus
Tilt and Backfocus
Future Work

## Slide 7: Scientific Workbench
Collect the right tools to iterate on new methods

## Slide 8
View measurements per star
No magic knobs, all parameters configurable
Re-analyze with different approaches
Visual inspection of each step of the process

## Slide 9: Star Annotation

## Slide 10: Star Rejection

## Slide 11: Tunable Parameters

## Slide 12: Test and Iterate

## Slide 13: Autofocus Replay

## Slide 14: Development Debugging

## Slide 15: Measuring Stars
Size, Shape, Center Position, etc

## Slide 16: Goals
Identify star candidates
Reject low-quality or poor matches
  Double stars
  Distorted
  Flat discs
Measure heuristic for star focus
  FWHM or HFR?

## Slide 17: 1 – Hotpixel Filtering
Simple (low-overhead) – 3x3 Median Blur
Thresholding (preferred) – Filter when large diff

## Slide 18: 2 – Noise Reduction
Gaussian Convolution
Stdev = Radius * 2 + 1

## Slide 19: 3 – Structure Detection
Wavelet to extract structures
Larger = bigger stars = longer focal length
Kappa Sigma background noise estimate
Larger = higher background noise
Dilate star candidate structures
Off by default
Binarize
Noise Clipping Multiplier * noise estimate
Star candidate boxes

## Slide 20: 4 - Rejection
Has saturated pixels
Touching border of image
Elongated/Distorted
Too dim
Centroid not centered
Too flat/no peak

## Slide 21: 5 – HFR Measurement
Sum of pixel brightness * center distance
Sum of pixel brightness
Distance containing half of star brightness

## Slide 22: 6 – FWHM Measurement
Point Spread Function
Non-linear optimization. No direct solution
B = background ADU
A = center ADU
x0, y0 = center
β = Moffat Beta (1.4)
σx, σy = FWHM sigma (solving for)
Convert sigma to FWHM pixels

## Slide 23: Autofocus
Finding Optimal Focus

## Slide 24: Hyperbolic Fit
HFR Std Dev
Minima
Goodness of Fit

## Slide 25: Doesn’t fit?

## Slide 26: Improvements
Outlier rejection
Hyperbola with different slopes
Minima changed by 34 steps
Higher error = lower weight

## Slide 27: Options

## Slide 28: Aberration Inspection
Measuring and correcting tilt and back-focus

## Slide 29: Background
Back-focus
Tilt
Similar, but at a gradient

## Slide 30: Corners Analysis
Credit: Chris White
Cloudy Nights Thread - https://www.cloudynights.com/topic/809050-tilt-discussion-astap/
Divide sensor into grid (3x3)
Calculate optimal focus in center and corners
No tilt = corners arrive at focus together
Perfect backfocus = corners arrive at focus with center

## Slide 31: Automated in NINA
Replay or run live
Large tilt!
Tilt and back-focus mixed together…

## Slide 32: Sensor Model
Credit: Frank Freestar8n
Observations
Calculate focus position for every star
Fit a 3d paraboloid across the sensor
Include a tilt plane to calculate both at the same time
Approach
Corners model coarse due to averaging across regions
Tilt must be corrected to measure back-focus error

## Slide 33: Mathematical Model
Distance from sensor center
Offset from curvature
Offset from tilt
Total offset
x0, y0 Sensor Center
c Positive or negative curvature inverse radius. Smaller = flatter
Θ, Φ Tilt plane rotation, amount (radians). Θ = 0 = no tilt
Variables

## Slide 35: Techniques Applied
Non-linear optimization - Levenberg-Marquardt
  Implemented with Alglib
Naïve star registration – Quad Trees
  Use RANSAC instead
Deal with outliers – Iterative reweighting (IRLS)

## Slide 36: Future Work

## Slide 37: Future Work
Autofocus
Fourier transformation method
  Credit: Cheng-Yan Tang
2-pass AF with FWHM and small step-size
Planetary AF in Fourier domain
Aberration Inspection
Guidance for which screws to turn
  Calculate tilt adjuster screw locations
  Motorized tilt adjusters?
Evaluate interpolation instead of outlier rejection
  Ie, Kriging and RBF

## Slide 38: Thank you
George Hilios
jokogeo (Discord)
ghilios (Cloudy Nights)